Hardware Component Specification – Line Stage

# Overview and Perspective
## Overview and Key Functions of System
This system is the first point of contact to amplify an auxillary signal. It is formed by two cascaded SRPP amplifier stages using a 6922/ECC88 dual triode vacuum tube. There is a negative feedback loop fed from the output to the cathode of the first SRPP stage. Gain is controlled by potentiometer RV1, which is a 10K potentiometer with one end bridged to the center, creating a 5K variable resistor. Gain is effectively RV1/R3. The Gain factor can be scaled from 0.003 to 15.15.
## Overview and Purpose of Hardware Component
The purpose of this component is to amplify an auxiliary audio signal to be a suitable level for the power amplification stage and to compensate for the losses from the passive filter circuit.
## Component Perspective

# Component Details
## Component Part Specification
- Qty. 2 ECC88 vacuum tubes
- Qty. 6 330 ohm 1/4W resistors
- Qty. 1 100K ohm 1/4W resistors
- Qty. 1 560K ohm 1/4W resistors
- Qty. 3 1uF 200V capacitors
- Qty. 1 10K ohm potentiometer
- Qty. 1 200pF 200V capacitor
## Signal/Communication Interface(s)
Input:
Auxiliary Audio
Output:
Post line-stage audio signal
## Power Interface(s)
Input:
170VDC power rail

## Key Properties/Functions
The system will output an amplified audio signal.