Hardware Component Specification – Line Stage

# Overview and Perspective
## Overview and Key Functions of System
This system allows the user to adjust the bass response, treble response, and volume level as desired. It is a passive system, which means the output voltage will be lower than the input voltage. For all three control dials, a 10K potentiometer is used. The bass and treble are adjustable to +/- 6dB. The volume control can attenuate the signal from 0% to 100% with steps of 1%.
## Overview and Purpose of Hardware Component
The purpose of this component is to adjust the bass characteristics, the treble characteristics, and the volume level per the listener’s preference.
## Component Perspective

# Component Details
## Component Part Specification
- Qty. 3 2.2K 1/4W resistors
- Qty. 2 1K 1/4W resistors
- Qty. 1 220nF 50V capacitor
- Qty. 1 10nF 50V capacitor
- Qty. 1 100K ¼W resistor
- Qty. 2 10K ohm potentiometer
## Signal/Communication Interface(s)
Input:
Post-Line stage audio signal
Output:
tuned post-line stage audio signal.
## Power Interface(s)
none

## Key Properties/Functions
The system will output a tuned audio signal suitable for power amplification.