# System Requirements Definition
## 1. Introduction
### 1.1 Purpose
This document specifies the system requirements for the Vacuum Tube audio amplifier. Its purpose is to transform the high-level stakeholder requirements into a technical view of a required product, defining what the system must possess and how it must perform from a supplier's perspective.
## 2. System Overview
### 2.1 System Boundary and Operational Environment
This section defines the functional boundary of the system. This establishes the expected system behavior at its boundary.
System's Stimuli and Responses
The following user inputs to the system shall be:
- Connect the desired audio source (eg. Phone, CD Player) to the system via line audio connection.
- Tune the desired gain using the provided knob.
- Tune the desired volume level using the provided knob.
- Tune the desired bass level using the provided knob.
- Tune the desired treble level using the provided knob.
The following output responses of the system will be:
Audio Playback.
Required Interactions and Interface Constraints
The system constraints are:
- Thermal – The system is not required to be operable below 0°C or above 85°C.
- Electrical – The system is only required to support a power supply of 120V AC.
Operational Environment
The system will be designed to operate in a primarily indoor environment around room temperature (25°C). It shall also be required to be operable in a mild outdoor environment within the temperatures specified above.

## 3. System Requirements Specification
This section details the required characteristics, attributes, and functional and performance requirements for the product solution.
### 3.1 Functional Requirements
The functions that the system is required to perform are defined as follows:
ID	Function/Requirement Description	Performance/Quantitative Measure
DW-001	The sound level of the system shall reach at minimum 79 dB SPL	79dB shall be measured using a sound level test device.
DW-002	There shall be provisions to attach modules for three types of audio sources: FM Radio, Bluetooth connection, line input via 3.5mm TRS jack. These modules shall be pluggable	The connection provision shall be present on the system and identified.
DW-003	One of the input modules shall be implemented at time of product launch	Module is present on system.
DW-004	The gain shall be adjustable at minimum from 0dB to 23 dB through a turn-knob.	Knob is present on the system, identified, and adjusts required level.
DW-005	The volume shall be adjustable from 10% to 100% signal level through a turn-knob.	Knob is present on the system, identified, and adjusts required level.
DW-006	The bass shall be adjustable at minimum from -6dB to 6dB through a turn-knob.	Knob is present on the system, identified, and adjusts required level.
DW-007	The treble shall be adjustable at minimum from -6dB to 6dB through a turn-knob.	Knob is present on the system, identified, and adjusts required level.
DW-008	The system shall be powered by US mains via a NEMA 1-15 or 5-15P.	The plug is present in the system.

### 3.2 Non-Functional Requirements
The non-functional requirements that the system is required to adhere to are defined as follows:
ID	Requirement Description	Quantitative Measure
DW-009	All Vacuum tubes in the system shall be visible outside of the product case.	The tubes are visible
DW-010	Vacuum tubes are connected to the system via socket to allow for easy replacement.	The tubes are socketed.
DW-011	Schematics are available for troubleshooting purposes	The schematics can be easily found online.
DW-012	All design files are readily accessible, including but not limited to PCB CAD files, 3d printed case files, analysis and design process documents, BOM.	All design files can be found online in the same location as the schematics.
DW-013	Project shall be released to the internet via public github and CC BY-NC-SA 4.0 licensed.	Project accessible through github publicly and released with CC BY-NC-SA 4.0 licensing.
DW-014	The project shall cost at or less than the price of 59 McDonald’s Big Macs to produce	The final constructed unit is produced for at or less than the given price.

## 4. Requirements Analysis and Verification Basis
### 4.1 Integrity
This section demonstrates the process for verification.
#### 4.1.1 Verification Basis
The system requirements will be satisfied and assessed. The following requirements will be verified in the following methods.
- Sound level – A testing apparatus will be used to ensure the sound output reaches 79 dB SPL.
- The input module connections will be present.
- All control knobs will be present.
- The Power connection will be present and accessible.
- All vacuum tubes in the system shall be visible and easily replaced via socket.
- The location of design files shall be known and navigable via the internet.
## 5. Functional Diagram